## Slide 1
USE CASE 3 • A DAY IN THE LIFE
Elena handles a failing bearing before it trips the unit
1
05:40
Anomaly flagged
Unit 2 at Station 14: vibration and bearing temperature have risen for three days.
2
06:10
Load shift approved
Likely thrust-bearing wear. Elena approves cutting Unit 2 to 70%, bound to that change.
3
07:30
Work order ready
Notification and work order drafted in SAP S/4HANA, bearing kit reserved.
4
10:20
Approval expires
A delayed adjustment reaches the gateway too late, so it is refused and asked again.
5
11:05
Data goes stale
Station 15’s feed lags, so the advisor drops to advice-only until it recovers.
6
13:20
Safety system acts
A gas detector trips Station 9’s shutdown on its own. Agents pause and advise.
7
14:00
Repair under permit
Qualified technicians start work under a permit approved on mobile.
8
18:30
Back in service
Elena approves the return to full load, and the event record is compiled.
Illustrative scenario. Elena Morales is a senior gas controller.
51
Notes: Tell Elena's day as a story.
At 05:40 the condition-monitoring agent flags Unit 2 at Station 14: vibration and bearing temperature have been rising for three days. By 06:00 the diagnostics agent has matched the pattern to two earlier thrust-bearing failures on the same model of unit and recommends an inspection within 24 hours at reduced load. At 06:10 the flow advisor proposes cutting Unit 2 to 70% and picking up the flow at Stations 13 and 15. The hydraulic model shows deliveries and pressures stay within limits. Elena approves at her console, next to the SCADA displays, and the change executes within its ten-minute window.
At 07:30 the planning agent has drafted the work order in SAP S/4HANA with the bearing kit reserved, and the planner releases it at 08:15. At 10:20 a second adjustment waits too long in the queue while Elena takes a shipper's call. Its approval has expired by the time it reaches the gateway, so it is refused and the advisor asks again with fresh values. When Station 15's data feed falls more than a minute behind at 11:05, the advisor drops to advice-only and voids a pending request until the feed recovers nine minutes later. At 13:20 a gas detector trips Station 9's emergency shutdown. The safety system acts on its own, and the agents pause requests for that segment and offer a re-balancing plan as advice. Qualified technicians start the repair at 14:00 under a permit their supervisor approved on mobile, and at 18:30 Elena approves the return to full load.
Leave the audience with this: people stayed in charge of every change to equipment, the safety systems never depended on the agents, and the repair happened in a planned window instead of after a trip.
Credit: John Fisher, The AI Control Plane: Executive Briefing (2026), slide 51, licensed under CC BY-NC-ND 4.0: https://creativecommons.org/licenses/by-nc-nd/4.0/. The full deck, with its speaker notes and notices: https://johnfisher-ai.github.io/ai-control-plane-handbook/deck/.