## Slide 1
USE CASE 3 • COMPONENT INTERACTION
How the components work together in Elena’s day
Control room & field
console • mobile
Orchestrator
dedicated ops tier
Specialist agents
A2A workers
Control plane
gateway • policy • identity
Models
ML • hydraulic • LLM
MCP servers & APIs
governed tools • DMZ
OT & systems
historian • SCADA • SAP
1 Historian replica: Unit 2 anomaly
2 A2A: score, diagnose, propose
3 Score (ML) and summarize (private LLM)
4 MCP calls with delegated token
5 Authorize read scopes and forward
6 Maintenance history and limits
7 Hydraulic check of the load shift
8 Tier 1: propose load shift
9 Controller approves the exact change
10 Check binding, expiry, cumulative limit
11 Setpoint request via the DMZ
12 Notification and work order
13 Refuse expired approval and ask again
14 Station 15 data stale: advice-only
15 Station 9 safety system trips on its own
16 Qualifications and permit
17 Supervisor and controller approve
18 Event record; back in service
Every hop emits an OpenTelemetry span and an audit event tied to the event ID. Approvals are bound and expire. Endnotes 26, 27, 78, 92, 94.
52
Notes: Read the numbered steps top to bottom. They follow Elena's day.
Steps 1–6 (05:40–06:00): the historian replica in the DMZ raises the anomaly, and the orchestrator delegates scoring and diagnosis over A2A [27]. The anomaly model scores Unit 2. The diagnostics agent reads maintenance history and engineering limits through MCP tools with a delegated token [92] and read-only scopes [26], and a private frontier model summarizes manufacturer guidance for the engineer.
Steps 7–11 (06:10): the Flow & Load Advisor runs the hydraulic check and proposes the load shift (Tier 1). Elena approves the exact change at the console. The control plane checks the binding, the ten-minute validity and the cumulative limit (custom Omni Gateway policies [78]). Only then does the setpoint-request service in the DMZ pass the change to the control system, which enforces its own engineering limits.
Step 12 (07:30): the planning agent creates the notification and work order through SAP S/4HANA tools.
Steps 13–15 (10:20–13:20): a delayed request is refused because its approval expired, and stale data from Station 15 drops the advisor to advice-only. When Station 9's safety system trips on its own, the agents only pause and advise.
Steps 16–18 (14:00–18:30): the crew agent confirms qualifications and drafts the permit, the supervisor and Elena approve, and the records agent compiles the event record. Every hop emits an OpenTelemetry span and an audit event [94].
Credit: John Fisher, The AI Control Plane: Executive Briefing (2026), slide 52, licensed under CC BY-NC-ND 4.0: https://creativecommons.org/licenses/by-nc-nd/4.0/. The full deck, with its speaker notes and notices: https://johnfisher-ai.github.io/ai-control-plane-handbook/deck/.
Bracketed numbers in these notes, and endnote numbers on the slide, refer to the endnotes in Appendix B of The AI Control Plane Handbook: https://johnfisher-ai.github.io/ai-control-plane-handbook/handbook/appendix-b.html.