## Slide 1
USE CASE 3 • AT A GLANCE
Anomaly to repair with a person on every equipment change
STAGE
PEOPLE
AGENT
CONTROL PLANE
MCP / API
SYSTEM OF RECORD
OUTCOME
Detect
No human step
Condition Monitoring
Tier 2 • scores only
Historian MCP (read)
Historian replica (DMZ)
Diagnose
Engineer decides
Diagnostics
Tier 1 • advises
SAP & document MCP
SAP S/4HANA • manuals
Stabilize
Controller approves
Flow & Load Advisor
Tier 1 • proposes
Setpoint request (gated)
SCADA via the DMZ
Plan work
Planner releases
Maintenance Planning
Tier 3 • notifications
SAP MCP (write)
SAP S/4HANA
Crew &
permit
Supervisor approves
Crew & Permit
Tier 2 • proposes
Workday & permit MCP
Workday • permits
Repair &
return
Controller approves
Compliance Records
Tier 2 • drafts
Event store MCP
Control room log
Enterprise AI control plane: registry • AI gateway • bound approvals • cumulative limits • agent identity • safe defaults • observability
Alert to planned repair in hours instead of days, with a controller approving every change to equipment and the safety systems independent throughout
Illustrative. Amber = human decision. Blue = agent and autonomy tier. Every call passes through the control plane.
49
Notes: Walk the six stages left to right. For each, point to the human step (amber), the agent and its autonomy tier (blue), and the governed path underneath: agents reach systems only through the control plane and a governed MCP tool or API, and nothing reaches the control system except through the DMZ.
Detect: the Condition Monitoring agent scores vibration, temperature and pressure trends from the historian replica (read-only, Tier 2).
Diagnose: the Diagnostics agent suggests likely causes from maintenance history, similar events and manufacturer guidance. The reliability engineer decides (Tier 1).
Stabilize: the Flow & Load Advisor proposes a load shift checked by the hydraulic model. The controller approves at the console, and the approval is bound to that exact change and valid for ten minutes (Tier 1).
Plan work: the Maintenance Planning agent creates the notification, drafts the work order and reserves parts in SAP S/4HANA. The planner releases it.
Crew & permit: the Crew & Permit agent confirms qualifications for the covered tasks [107] and drafts the isolation permit. The field supervisor approves on mobile.
Repair & return: the controller approves the return to full load. The Compliance Records agent assembles the event record.
The outcome to land: alert to planned repair in hours instead of days (illustrative), with a controller approving every change to equipment and the safety systems independent throughout.
Credit: John Fisher, The AI Control Plane: Executive Briefing (2026), slide 49, licensed under CC BY-NC-ND 4.0: https://creativecommons.org/licenses/by-nc-nd/4.0/. The full deck, with its speaker notes and notices: https://johnfisher-ai.github.io/ai-control-plane-handbook/deck/. You may adapt this slide, with credit, under the additional permission in the deck’s notices: https://johnfisher-ai.github.io/ai-control-plane-handbook/deck/notices.html#permission.
Bracketed numbers in these notes, and endnote numbers on the slide, refer to the endnotes in Appendix B of The AI Control Plane Handbook: https://johnfisher-ai.github.io/ai-control-plane-handbook/handbook/appendix-b.html.