## Slide 1
TRUST • PHYSICAL OPERATIONS
When agents can move equipment
In energy, utilities and industrial operations, the control plane governs what agents may request. Independent safety layers decide what equipment may do.
AGENTS & CONTROL PLANE
Enterprise zone or industrial DMZ: agents propose and Agent Fabric enforces identity, policy, bound approvals and cumulative limits
INDUSTRIAL DMZ
Historian replica (read-only) and a setpoint-request service: the only conduit into operations
CONTROL SYSTEM
SCADA or DCS enforces engineering limits, and the controller approves each change at the console
INDEPENDENT SAFETY LAYER
Safety instrumented systems, emergency shutdown and interlocks act on their own. No agent can reach them
PHYSICAL SAFEGUARDS
Relief valves and mechanical protection: the last line of defense
Requests flow down only through governed conduits
No agent path
DESIGN RULES
1
Agents propose, people approve
Each approval is bound to the exact change and valid for minutes, not hours.
2
Keep safety independent
No agent tool reads or writes safety logic or bypasses an interlock.
3
Limit the total across steps
Caps on cumulative change apply across agents and sessions.
4
Fail to the engineered safe state
Stale data or lost contact drops agents to advice-only. Process safety defines the safe state.
Sources: endnotes 32, 66–69. Reference use case 3 applies these rules to a gas pipeline operator.
20
Notes: Key point: when an agent's action can reach physical equipment, the gateway is not the last line of defense. The control plane governs what agents may request, while independent safety layers decide what equipment may do.
The layers, top to bottom: agents and the control plane sit in the enterprise zone or industrial DMZ. Next is the DMZ itself, with a read-only historian replica and a setpoint-request service as the only conduit into operations. Below it is the control system, which enforces engineering limits and where the controller approves each change. Then comes the independent safety layer (safety instrumented systems, emergency shutdown, interlocks), which acts on its own under process-safety discipline [66]. Physical safeguards such as relief valves sit at the bottom.
Current guidance from US, Australian and allied cybersecurity agencies is explicit: people remain responsible for functional safety, AI should not actively control OT without a human in the loop, and AI systems need failsafes so they fail gracefully without disrupting critical operations [67]. Keep agents out of the control network and reach control systems only through defined conduits, following the ISA/IEC 62443 zone-and-conduit model and NIST's guide to OT security [68][69].
The four design rules on the right become runtime enforcement through custom Omni Gateway policies: Approval-to-Execution Binding checks that what executes is exactly what was approved and that the approval has not expired, and the Cross-Session Aggregate-Risk Gate caps cumulative change across agents and sessions [78]. When data goes stale, fall back to the safe state that process-safety engineering defines, which is not always "stop."
Regulation points the same way: under the EU AI Act, AI used as a safety component in the supply of water, gas, heating or electricity is high-risk, with human-oversight obligations from December 2027 [32]. Reference use case 3 shows the pattern at a natural gas pipeline operator.
Credit: John Fisher, The AI Control Plane: Executive Briefing (2026), slide 20, licensed under CC BY-NC-ND 4.0: https://creativecommons.org/licenses/by-nc-nd/4.0/. The full deck, with its speaker notes and notices: https://johnfisher-ai.github.io/ai-control-plane-handbook/deck/.
Bracketed numbers in these notes, and endnote numbers on the slide, refer to the endnotes in Appendix B of The AI Control Plane Handbook: https://johnfisher-ai.github.io/ai-control-plane-handbook/handbook/appendix-b.html.